## Slide 1: Media Optimization for Biofuels from Cyclotella cryptica
Alyssa Keptner, Dr. Jacob Borden McKetta Department of Chemical and Bioprocess Engineering

## Slide 2: Research Goals
Overall goal is to use the lipids in diatoms to make biofuels
Maximize growth of diatoms for lipid productivity

## Slide 3: Introduction
Working with diatom species Cyclotella cryptica (C. cryptica)
Notes: Diatoms are main component of phytoplankton
Diatoms have a silica shell making them unique compared to green algae
Working with diatom species Cyclotella cryptica
C. cryptica are about 40% lipids, and about 55% of that was triacylglycerol (TAG)

## Slide 4: Experimental Set-Up
Grow tent at 21 °C
Grow light- 18 hours on, 6 hours off
Shaker plate for aeration & mixing

## Slide 5: Overall Growth Determined Using Optical Density
Measured using absorbance on a plate reader at 436 nm
No mathematical correlation from OD to cell density
Triplicates of data were taken, average was used to find normalized OD

## Slide 6: Media Base Components
Lab created seawater- 28 g/L NaCl
Growth additives
  NaNO3
  NaH2PO4·H2O
  Na2SiO3 · 9H2O
  Trace Element Solution
  Vitamin Solution

## Slide 7: Real Seawater vs Lab Created Seawater
Real seawater pulled from Boston Harbor in the fall of 2021
Notes: 21 David G Mugar Way, Boston, MA 02114

## Slide 8: Boston Seawater vs Lab Created Seawater
Boston seawater base resulted in better growth than lab created seawater base by a factor of 7.6
Notes: Real seawater trials were completed with water from Boston harbor (pulled in Fall of 2021 for AIChE Nationals)
Difference was that 1 was all fake seawater, 1 was all real seawater
250 mL total volume
8 days of growth
450% change of real seawater or a 60% change of lab created

## Slide 9: Boston Seawater vs Lab Created Seawater
Normalized OD and actual OD show similar results- use normalized OD

## Slide 10: Real Seawater Grows C. cryptica Better
Some nutrient(s) present in real seawater that are absent or in lesser concentration in lab created seawater
Next step- Test growth additives to see if any additives majorly affect growth
Lab Created
Boston

## Slide 11: Design of Experiments (DOE)
Determining what growth additives have a statistical impact on C. cryptica growth
Five growth additives
  NaNO3 (1x is 0.882 mM)
  NaH2PO4·H2O (1x is 0.0362 mM)
  Na2SiO3 · 9H2O (1x is 0.106 mM)
  Trace Element Solution (1x is 1 mL/1000L)
  Vitamin Solution (1x is 0.5 mL/1000L)
Varied concentration
  High (2x)
  Medium (1x)
  Low (0.5x)

## Slide 12: DOE
65 total trials- 2mL total volume
Grow Light
Shaker Plate
Well Plate

## Slide 13: DOE Results
Silica was the only growth additive with a statistical impact on C. cryptica growth

## Slide 14: Varying Silica Concentration
1x is 0.106 mM
Trial 1: 0.5x, 1x, 5x
Trial 2: 1x, 2x, 3x, 4x
Silica concentration
Heteropoly blue method (Hach reagent set)
Absorbance on plate reader
Lipid concentration
Nile red staining
Fluorescence on flow cytometer
Grow Light
Notes: Heteropoly Blue method tested using a microplate reader read at OD 815 nm
Flow cytometer excitation was 488 nm, emission was 695 nm for Nile red
No agitation, could impact results slightly but not by much

## Slide 15: Trial 1- Normalized Optical Density
1x concentration was the best, 5x concentration showed no growth
Varying Silica Concentration

## Slide 16: Trial 2- Normalized Optical Density
2x concentration was the best, at too high of a silica concentration growth begins to decrease
Varying Silica Concentration

## Slide 17: Trial 1- Testing Media Silica Concentration
Varying Silica Concentration

## Slide 18: Trial 2- Testing Media Silica Concentration
Varying Silica Concentration

## Slide 19: Testing Media Silica Concentration Conclusions
Inconsistent results between trial 1 and trial 2
Need a better method to measure silica concentration in media throughout the trial
Redo growth trials

## Slide 20: Trial 1- Lipid Density at 331 Hours
5x concentration had no lipid growth
Varying Silica Concentration
Intensity
Intensity
Intensity
Notes: X-axis is intensity
Y-axis is the cell count (difference between the count is the difference between trials, constant volume was pulled)
Chart is showing how many cells have that intensity, big peak is showing there are a bunch of cells with not much excitation, but the smaller peak shows a few cells that do have that fat or lipid

## Slide 21: Trial 2- Lipid Density at 336 Hours
2x concentration had best lipid growth
Varying Silica Concentration
Intensity
Intensity
Intensity
Intensity
Notes: X-axis is intensity
Y-axis is the cell count (difference between the count is the difference between trials, constant volume was pulled)
Chart is showing how many cells have that intensity, big peak is showing there are a bunch of cells with not much excitation, but the smaller peak shows a few cells that do have that fat or lipid

## Slide 22: Conclusions- Lipid Density
2x concentration of silica had the highest peak of lipid density compared to overall cell density
Intensity

## Slide 23: Future Studies
Water quality testing to determine what is in the Boston seawater
  Real seawater media base showed 2x more silica than lab created seawater media base
Two stage growth for maximizing lipid growth
  Nutrient replete & nutrient deplete
Lipid extraction (transesterification, bead milling)
d’Ippolito, G., Sardo, A., Paris, D. et al. Potential of lipid metabolism in marine diatoms for biofuel production. Biotechnol Biofuels 8, 28 (2015). https://doi.org/10.1186/s13068-015-0212-4

## Slide 24: Conclusions
Out of the five growth additives put in media base, silica was the only additive with a statistical impact on overall C. cryptica growth
Silica concentration of 0.212 mM lead to the best overall growth and lipid growth in C. cryptica
Real seawater contains many nutrients not present in lab created- lead to better overall growth

## Slide 25: Acknowledgements
Dr. Samuel Drerup for starting sample of C. cryptica
Rinker Ross School of Health Sciences, Trine University
Funding by the McKetta Department of Chemical and Bioprocess Engineering, Trine University
Dr. Jacob Borden

## Slide 26: References
Guillard, R. R. L., & Hargraves, P. E. (1993). Stichochrysis immobilis is a diatom, not a chrysophyte. Phycologia, 32(3), 234–236. https://doi.org/10.2216/i0031-8884-32-3-234.1
Hildebrand, M., Davis, A. K., Smith, S. R., Traller, J. C., & Abbriano, R. (2012). The place of diatoms in the biofuels industry. Biofuels, 3(2), 221–240. https://doi.org/10.4155/bfs.11.157
d’Ippolito, G., Sardo, A., Paris, D. et al. Potential of lipid metabolism in marine diatoms for biofuel production. Biotechnol Biofuels 8, 28 (2015). https://doi.org/10.1186/s13068-015-0212-4
Gao G, Wu M, Fu Q, Li X, Xu J. A two-stage model with nitrogen and silicon limitation enhances lipid productivity and biodiesel features of the marine bloom-forming diatom Skeletonema costatum. Bioresour Technol. 2019 Oct;289:121717. doi: 10.1016/j.biortech.2019.121717. Epub 2019 Jun 27. PMID: 31279322.

## Slide 27: Questions?
Out of the five growth additives put in media base, silica was the only additive with a statistical impact on overall C. cryptica growth
Silica concentration of 0.212 mM lead to the best overall growth and lipid growth in C. cryptica
Real seawater contains many nutrients not present in lab created- lead to better overall growth

## Slide 28: Appendix

## Slide 29: Growth Additives
L1 marine media component list and concentrations (based on 1 L total volume)

## Slide 30: Microplate Reader- SpectraMax iD3
Overall Optical Density: Absorbance- 436 nm
Nile Red Method: Fluorescence- Excitation 488 nm, Emission 695 nm
Heteropoly Blue Method: Absorbance- 815 nm

## Slide 31: Heteropoly Blue Method
Hach Reagent Set
10 mL total volume
Testing for 0.01-1.6 mg/L SiO2
Molybdate 3 Solution
Citric Acid Reagent
  Destruction of phosphate interference
Amino Acid F Reagent
  Blue color indicates silica is present

## Slide 32: Trial 1- Optical Density
1x concentration was the best, 5x concentration showed no growth
Varying Silica Concentration

## Slide 33: Trial 2- Optical Density
2x concentration was the best, too high of a silica concentration begins to decrease growth
Varying Silica Concentration